Suite Plants Living Walls are the best way to give your space a “green” image. Living Walls are a cutting edge design element that makes a dramatic statement and creates a welcoming environment for employees, clients and visitors.  They can be installed both indoors and outdoors. According to studies, Living Walls can clean pollutants from the air, lower occupant stress, increase property values and improve worker productivity. All Suite Plants products use a cloth wick system to deliver water to the plants, so there is no need for pumps or drip lines.  Review specifications below for applicability to your project; delete paragraphs not required.

SECTION 12 94 00

LIVING WALL SYSTEMS

GENERAL

SUMMARY

Provide living wall systems for interior applications.

Provide living wall systems for exterior applications.

RELATED WORK

Division 22 – Plumbing for coordination with water supply and connections.

Division 26 – Electrical for coordination with lighting fixture type and location to ensure 150 footcandles for applications that are using low light tropical plant.

SUBMITTALS

Product Data:  Submit manufacturer's literature including product characteristics and maintenance data.

Shop Drawings:  Submit diagram showing living wall system size and configuration, including details of perimeter conditions and mounting.

Verification of Light Level:  Measure the footcandle light level in the location of the living wall system accounting for both ambient light and light from fixtures.  Submit written report listing date of test and results.

Maintenance Data:  For each product installed.

QUALITY ASSURANCE

Installer:  Experienced with installation of similar products, and acceptable to the manufacturer.

Mock-Ups:  For projects with multiple installations, the first installed system shall be considered a mock-up.  Obtain Architect’s acceptance of first installation before performing subsequent installations.

DELIVERY, STORAGE AND HANDLING

Products:  Deliver products in unopened factory labeled packages. Store and handle in strict compliance with manufacturer's instructions and recommendations.

FIELD CONDITIONS

Field Measurements:  Verify existing dimensions prior to preparation of shop drawings to the greatest extent practical.

Planting Restrictions:  If plants are provided, do not install plants until building systems are operational and will maintain stable temperature conditions.

WARRANTY

Manufacturer’s Warranty:  Provide manufacturer’s standard limited warranty for materials.

PRODUCTS

MANUFACTURER

Basis-of-Design Manufacturer:  Suite Plants, 2 Maple Road, Cornwall-on-Hudson, NY 12520.  Tel. 855-275-8111, www.suiteplants.com, info@suiteplants.com.

LivePanel:  Modular living wall system by Suite Plants.

Water Efficiency:  100 percent water efficient; no wastewater generated.

Weight Per Square Foot: 8.2 pounds per square foot typical, including plants and water.

Plants Per Square Foot:  4.5 typical, depending on species.

Water Use:  0.65 gallons per 10 square foot per week typical.

Cassettes:  Fabricated from EPP (expanded polystyrene), 15.75 high by 15.75 inches wide by 2.22 inches deep, with nine four-inch plants per cassette.  Cotton wick throughout to deliver water by capillary action.  Waterproof backing.

Gutters:  Extruded anodized aluminum, acting as water reservoir.  Predrilled mounting holes, clips to secure cassettes below, solid watertight end caps at one end, hose cap connection at the other end.

Hoses:  To connect each gutter to gutter below and allow water to cascade from one gutter to the next.

Fasteners:  As recommended by manufacturer based on site conditions.

Irrigation:  Manufacturer’s standard irrigation unit, UL listed, 110VAC.

Decorative Frame:

Interior: Satin anodized aluminum silver-color or black textured vinyl frame, approximately 2-1/2 inches wide by 2-1/2 inches deep, to cover hose, end caps, gutters.

Exterior: Extruded aluminum silver-color frame approximately 7 inches wide by 2-1/2 inches deep, mitered corners, to cover hose, end caps, gutters.

Plants:  Pre-grown plants in pots, variety as selected by Architect.

Plants:  None, furnished by others.

EXECUTION

EXAMINATION

Examine substrates for compliance with requirements for installation tolerances and other conditions affecting performance.  Proceed with installation only after unsatisfactory conditions have been corrected.

Verify lighting fixtures or ambient light provide 150 footcandles.  Notify Architect in writing if this requirement is not met.

INSTALLATION

Install products in strict accordance with manufacturer’s instructions and approved submittals.

Follow manufacturer’s recommendations for attachment.

Install in compliance with ADA guidelines for location.

Replace damaged units prior to Substantial Completion.

If plants are installed as part of the work of this section, provide watering and maintenance until turnover to Owner’s personnel.  Demonstrate proper watering and maintenance procedures to Owner’s designated personnel.

CLEANING

Clean surfaces to remove soiling, stains, dust, and dirt using materials acceptable to manufacturer.

Leave installation area clean, free of residue and debris resulting from work of this Section.

END OF SECTION